Software Design

25. March 2015
2IO70

The purpose of this document is to present a Java program that realises the functions specified in the Software Specification document. This program is an intermediate step towards writing the PP2 code that controls the sorting machine.

Group 16
Rolf Verschuuren
Wigger Boelens
Stefan van den Berg
Dat Phung
Maarten Keet
Tudor Petrescu
Version 1

# Coding Standards
The java pseudo code follows the Google Java Style.
Source to Google Java Style: https://google-styleguide.googlecode.com/svn/trunk/javaguide.html.
Php code used in this project follows the Zend Framework Coding Standard for PHP.
Source: http://framework.zend.com/manual/1.12/en/coding-standard.html.
Translating to pseudo java:
The java program starts by declaring the output variables. The names of the output variables will keep their original name, without spaces, in a camelCase form. The variable type will be determined from the Output table.
The inputs follow the same pattern.
Every states is represented as a function, keeping their name in the camelCase fashion, they will be all void functions due to the fact that they do not return anything.
Every state function will run preconditions if any, then check for specific input values using if statements, if an if statement is satisfied, there will be changes to the output values to match the next states output values, also the display is set to output the next states number, and then the next state function is called according to the state transition diagram, if no if statement is satisfied the current function is recalled.
The program is always looping, consequence of no deadlocks in the state machine as proven by the uppaal model test.
Example: Initial -> Calibrate_Sensor
So in this example the function initial is currently running, there are no preconditions to be checked, if the inputs have the desired value, in our case we check if the push button is pressed by the sorter, if so we will have the sorter moved down by activating the sorter motor via having the Hbridge0 variable set to 1. After this we set the display to showcase the number $branchTO where to branch to2 then call calibrateSensor function and if the if statement wasn’t satisfied we recall initial entering a loop.
## Translating from java to php:
The java code was written such that the conversion process to php is as easy as possible.
All variable in java will have the “$” sign added at the beginning of their name to comply with the php standards. The “$” sign has no influence in the java program variable naming, while in php it is mandatory.
## Design decisions for the Java code
In translating our transition table to a Java program we made a number of decisions shaping the code, these decisions are outlined in this section.
We started by looking at our transition table, in this table we had our transitions ordered by the “current state”, the state where the transition starts. Then there were some inputs that could trigger a transition from this state to a number of other states. Because of this we thought it would make sense to write a function for each state, since it would allow our code to essentially be a condensed version of the transition table. Where the code would be ordered by the “current state”, and each state would have a number of outgoing transitions to other states. This resulted in the following blueprint for each of our functions:
void function(){
   timerManage();	// The function that manages the outputs and PWM
   $temp = getButtons();	// Store the buttons currently being pressed in a temporary variable

   if( condition for transition ){	// Do this once for every outgoing transition from this state
      Changes required to change to the new statement;
   }

   function();	// Call on the same function again to recheck the buttons and continue
running the machine with timerManage()
}

Then we made an extra function which will be called from each function to do the PWM. This function is called timerManage. This function firstly gets the voltage which the output needs from the array.
This function has a variable called counter which increments each time the outputs have been set. That value is take modulo 12. So it will leave the outputs which need 12 volts on all the time. The reason why the values which need less than 12 volt will be turned off after they have been on for long enough. That goes as follows. First it checks if the engine needs to be on by checking if the voltage it needs is higher than counter. If the output needs to be on then it gets the location of the value in the array. And then does 2 to the power of the location. So now the correct output will be set on. Then the value of 2 to the power will be added to the variable engines. Then after all 7 outputs have been through that loop then it will set the output to the value of engines. So the lights which needed to be on will be on. Now the value of counter will increment each time and take modulo 12.

We also choose to save certain values, which may not be expected to be saved. In this section I will explain why we save the 2 variables. The first one is the variable of the location of the code. This has been saved because then we then we are capable of changing the return address after the timer interrupt. Because when an timer interrupt occurs we want to return to the initial state and the position where we were before. We also saved the original position of the stack pointer for when we come back from the timer interrupt to make sure that we empty the stack. Because there may be some values on the stack from before the timer interrupt. Thus to remove them we set the stack pointer to its original value.

# Validation
## Validation of java to transition table
Every state is represented by a function. The if statements in that function are the transitions which can occur from that state. The timer interrupt and the abort transitions are not represented as if statements, because interrupts go to a separate state(function). In those if statements the values that have to change are changed. The display will also be updated to the correct number of the state. The function timerManage is called in each state. Because with that function we make sure that the all outputs have the correct voltage.
We checked that all states are represented in the java code by a function. We also checked if they have all the transitions as if statements and that the correct values are changed.
## Validation of timerManage
Loop invariant:
All elements before the current element of the array have been set on if they had to be on.
Initialize:
We start with the first element. Thus there are no elements before it and the loop invariant holds.
Step case:
If we’re at element k, then according to the loop invariant all elements before k have been set on if they had to be on. Then if k has to be on (value of k>counter) it will be set on else it will stay off. So now the loop invariant holds for the element k+1
Termination:
The loop will terminate when k is greater than 7. Because we do not have any more outputs.
## Control flow validation
Because the Java code has been validated to the state description and the transition table, which, in turn, have been validated with the UPPAAL model and shown to be correct and in tune with the initial description of the sorting machine. This means that the Java program, being a one-to-one translation of the finite state automaton, also has a correct control flow.
Explanation of the compiler functions
storeRam($location, $value)
Store a value in the ram.
$location	The location (a variable) to store the value in the ram
$value	The value to store, needs to be a variable
return	void
getRam($location)
Get a value from the ram.
$location	The location (a variable) where the value is stored
return	The value that is stored at the location
display($what, $onWhat, $location = '000001')
Display something on either the display or the leds.
Possible values for $onwhat:
- leds: the leds at the top
- leds2: the leds to the right
- display: the display
$what	What to display, must be a variable
$onWhat	On what to display
$location	Where to show the value when using the display, defaults to the right position
return	void
pow($number,$power)
Get the power of a number
$number	The number to power
$power	The power value
return	Int; The result
mod($what, $variable)
Take the modulo of a number
$what	Modulo what
$variable	Variable to modulo over
return	void
getInput($writeTo, $type)
Get button or analog input. When you just want the input of 1 button, use getButtonPressed instead.
$writeTo	Variable to write the input to
$type	Type of input, possible values are: buttons, analog
return	void
getButtonPressed($button)
Check if a button is pressed. Puts the result into R5.
$button	Which button to check (input a variable)
return	Int; Whether or not the button is pressed.
installCountdown($functionName)
Install the countdown.
$functionName	The name of the function where the timer should go to
return	void
startCountdown()
Start the countdown.
Retrun	void
pushStack($variable)
Push a variable to the stack
$variable	The variable to push to the stack
return	void
pullStack($variable)
Pull a variable from the stack.
$variable	The variable where the pulled variable is put into
return	void
setCountdown($countdown)
Set the timer interrupt to a value. It will first reset the timer to 0.
$countdown	How long the countdown should wait, in timer ticks
return	void
getData($location, $offset)
Get data. Use offset 0 when it is just a single value.
$location	The location where the variable is stored
$offset	The offset of the location
return	The value of the data segment
storeData($variable, $location, $offset)
Store data. Use offset 0 when it is just a single value.
$variable	The variable to store
$location	The name of the location where the variable is stored
$offset	The offset of the location
return	void
sleep($howLong)
Pause the program.
$howLong	How long to sleep in clockticks
return	void
initVar($variable,$places)
Initialize a variable that is used in that data segment.
$variable	The name of the variable
$places	How long the array is
return	void
branch($branchTO)
Branch to a function.
$branchTO	where to branch to
return	void
moveFunction($branchTO)
Move a function in the assembly code.
$branchTO	Where to branch to
return	void
# Appendix: Java Program (Compiler?)