Software Specification

11th of March 2015
2IO70
Version 0.8

The purpose of this document is to give an as accurately as possible description of the required behaviour of the PP2, without describing how this is achieved, and a UPPAAL model of this behaviour. In order to do this, we translate the system level requirements to a high level specification of what the software controlling the physical machine should do.

Group 16
Rolf Verschuuren
Wigger Boelens
Stefan van den Berg
Dat Phung
Maarten Keet
Tudor Petrescu

Validation Machine Design to Software Specification
The inputs of the Machine Design phase, specifically the system level requirements, are the outputs of Software Specification. Machine Design forms the physical machine built from Fisher Technik components, while Software Specification defines the software that controls the machine.
# Inputs and Outputs
## Inputs
Input	The range/type of the value
Start/Stop button	Boolean value
Abort button	Boolean value
Push button(sensor)	Boolean value
Position sensor	Boolean value
Colour detector	Boolean value
Timer	Values range from seconds to clock ticks, consists of TEnd, Motor Down, Motor Up, Sort, Belt, and Tic

Timers
All given times are calculated by taking the average time of ten measurements.
TEnd is the moment of termination of the timer, so when the timer reaches zero. The timer is a count-down timer that is set to a certain value and runs at a frequency of 10 kHz.
Motor Down is defined as the time it takes for the engine of the sorter to move the sorter from the lowest point to the highest point, until sorting mechanism touches the push sensor. This takes 0.30 seconds.
Motor Up is the state of the sorter moving from the highest point to the bottom of the engine sorter. Since the engine sorter for Motor Down and Motor Up have the same voltage, this will take 0.30 seconds as well.
Sort is the amount of time it takes for a disc to be transported from the black/white detector to the end of the conveyor belt, which is measured to be 0.85 seconds.
Belt is the period that a disc travels from the feeder to the end of the conveyor belt, until the disc reaches the tray for black discs. This action takes 2.0 seconds.
Tic is defined as one clock tick of the PP2. A clock tick is incredibly fast.
## Outputs
Output	The range/type of the value
Lens lamp position	Boolean value
Lens lamp sorter	Boolean value
Conveyor engine	Between 6 and 9 V while running / 0 V when not running
Feeder engine	Between 3 and 7 V while running / 0 V when not running
Hbridge0	Boolean value, current is between 6 and 9 V while running
Hbridge1	Boolean value, current is between 6 and 9 V while running
Display	Integer value, positive
LED state indicator	Boolean value, indicates whether it’s in the resting state or not
Timer start	How long the timer runs in seconds.

Validation Inputs/outputs to Machine Design
We see that the inputs and outputs of Software Specification are correct. The inputs of Machine Design should be equal to the outputs of Software Specification, which they are.
## Relations
Lens lamp of the black white detector
The lens lamp of the black white detector will be on when the machine is sorting. Thus the lens lamp will react to the input of the “START/STOP” button and the “ABORT” button. The lens lamp will go on when the machine is in resting state and the “START/STOP” button is pressed and it will go off when the “ABORT” button is pressed while the machine was running.
Lens lamp of the position sensor
The lens lamp of the position sensor reacts only to the “START/STOP” button and the “ABORT” button. The lens lamp will be on after the “START/STOP” button is pressed and the machine is in its resting state. If at any other point in time the “ABORT” button is pressed it will go off. When the “START/STOP” button is pressed and the machine is running then the lens lamp also goes off.
Engine of the conveyor belt
The engine of on the conveyor belt only reacts to the input of the “START/STOP” button and the “ABORT” button. The engine will start when the machine is in its resting state and the “START/STOP” button is pressed. If however the “START/STOP” button is pressed and the machine is not in its resting state then the machine will stop after it completed its current cycle. Whenever the “ABORT” button is pressed the engine stops within 50ms.
Engine of the feeder
The engine for the feeder also only reacts to the input of the “START/STOP” button and the “ABORT” button. This engine also starts when the machine is in its resting state and the “START/STOP” button is pressed. If however the machine is running then the engine will stop. When the “ABORT” button is pressed the engine stops within 50ms.
Engine for the sorter
When the machine is running the engine of the sorter reacts to inputs of the colour detector, the push sensor and the timer. When a signal is received from the colour detector the engine pushes the sorter up, the engine then waits until the timer gives a signal to go down again after it let the disks through, it knows when it is in the correct “up” position from the push sensor . If the “START/STOP” button is pressed when the machine is in its resting state, then the sorter will wait for a signal from the timer that marks the end of the current cycle. If at any time the ““ABORT”” button is pressed, the sorting mechanism is to stop within 50ms.
Display for counting
The display output depends on how many times the colour detector detects a white disc and how many times a disc passes the position sensor without the colour detector detecting it.
In the initial state the counters get reset.
### Validation of the Relations
The relations between the inputs and outputs can be validated with the input/output tables. For all inputs, we have outputs. These outputs depend on one or more inputs, which is described in the Relations.
# Description of States
Initial_state
Outputs	Value for output
Lens lamp position	0
Lens lamp sorter	0
Engine conveyor	0
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	0

Calibrate_Sorter
Outputs	Value for output
Lens lamp position	0
Lens lamp sorter	0
Engine conveyor	0
Engine feeder	0
Hbridge0	1
Hbridge1	0
Display	0
LED state indicator	0
Timer start	0

Resting_state
Outputs	Value for output
Lens lamp	0
Lens lamp	0
Engine conveyor	0
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	1
Timer start	0

Running_state
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	2 s + Belt

Running_Wait
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	2 s + Belt

Running_Timer_Reset
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	2 s + Belt

Motor_Up
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	1
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Sort

Motor_Up_Stop
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	1
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Sort

Motor_Down
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	1
Display	0
LED state indicator	0
Timer start	0

Motor_Down_Stop
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	1
Display	0
LED state indicator	0
Timer start	0

White_Wait
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Sort

White_Wait_Stop
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	1
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Sort

Runing_Timer
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Belt

Motor_Up_Timer
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Belt

White_Wait_Timer
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Belt

Motor_Down_Timer
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	Belt

Aborted
Outputs	Value for output
Lens lamp position	0
Lens lamp sorter	0
Engine conveyor	0
Engine feeder	0
Hbridge0	0
Hbridge1	0
Display	0
LED state indicator	0
Timer start	0

After_tick
Outputs	Value for output
Lens lamp position	1
Lens lamp sorter	1
Engine conveyor	1
Engine feeder	0
Hbridge0	0
Hbridge1	0
Engine sorter	0
Display	0
LED state indicator	0
Timer start	Belt

### Validation of the state description
The validation for this part is not yet completed and will be added at a later moment in time.
# State transitions
Current state	Input	Input value	Next State
Initial	Push	1	Calibrate_Sorter
Calibrate_Sorter	Push	0	Resting
Resting	StartStop	1	Running
Running	Timer	TEnd	Initial
Running	PositionSensor	0	Running_Wait
Running	Abort	1	Aborted
Running	StartStop	1	Running_Timer
Running_Wait	Timer	TEnd	Initial
Running_Wait	PositionSensor	0	Running_Timer_Reset
Running_Wait	ColorDetector	1	MotorUp
Running_Wait	StartStop	1	Running_Timer
Running_Wait	Abort	1	Aborted
Running_Timer_Reset	Tick	1	Running_Wait
Running_Timer_Reset	Abort	1	Aborted
MotorUp	PushButton	1	WhiteWait
MotorUp	StartStop	1	Motor_Up_Timer
MotorUp	Abort	1	Aborted
WhiteWait	StartStop	1	White_Wait_Timer
WhiteWait	Abort	1	Aborted
WhiteWait	Timer	SORT	MotorDown
MotorDown	StartStop	1	Motor_Down_Timer
MotorDown	Abort	1	Aborted
MotorDown	Timer	Motor Down	Running_Wait
Running_Timer	Timer	Tic	After_tick
Running_Timer	Abort	1	Aborted
Motor_Up_Timer	Timer	Tic	Motor_Up_Stop
Motor_Up_Timer	Abort	1	Aborted
White_Wait_Timer	Timer	Tic	White_Wait_Stop
White_Wait_Timer	Abort	1	Aborted
Motor_Down_Timer	Timer	Tic	Motor_Down_Stop
Motor_Down_Timer	Abort	1	Aborted
Motor_Up_Stop	PushButton	1	White_Wait_Stop
Motor_Up_Stop	Abort	1	After_tick
Motor_Up_Stop	Timer	Timer Interrupt	Initial
Motor_Up_Stop	Abort	1	Aborted
White_Wait_Stop	Timer	SORT	Motor_Down_Stop
White_Wait_Stop	Abort	1	Aborted
White_Wait_Stop	Timer	Timer Interrupt	Initial
Motor_Down_Stop	Timer	Motor Down	After_tick
Motor_Down_Stop	Abort	1	Aborted
Motor_Down_Stop	Timer	Timer Interrupt	Initial
After_tick	ColorDetector	1	Motor_Up_Stop
After_tick	Abort	1	Aborted
After_tick	Timer	Timer Interrupt	Initial
Aborted	StartStop	1	Initial

### Validation of the state transitions
The description of our machine states is validated through its representation in the transition table. No state is excluded from being represented in the state transition table, all transitions will have the initial transition state differ from the end state.

# Finite state Automaton
### Validation of the finite state automaton
When we were making our finite state automaton we looked at our state description and made sure that all states were represented, then we used our state transition table to make sure all transitions were correctly implemented.
# UPPAAL model
## Tests done
On the next page is the UPPAAL model. This UPPAAL model has been tested for 2 safety properties. The first one is “ After the start-up of the machine, the assembly program should not stop until the machine is shut down.”. This has been tested using the following property “A[] not deadlock”, and we didn’t have a deadlock. The second safety property which was tested is: “The outputs connected to the h-bridge may never be powered on at the same time.”. This was tested using the following property “A<> !(hbridge0==1 && hbridge1=1)”. This one was also correct.
### Validation of the UPPAAL model
All transitions which exist in the UPPAAL model also occur in the Finite State Automaton. And the same action has to be performed to take that transition. Also all states of the Finite State Automaton occur in the UPPAAL model. The states of the UPPAAL model also have the outputs in them. The states of the Finite State Automaton do not have the outputs in them. Thus we validate the values of the outputs, which are in the states, to the description of the states.
Validation Safety Properties to UPPAAL

Safety property 3 can be validated by looking at the UPPAAL model: after the start-up of the machine, the assembly program should not stop until the machine is shut down. There are states with incoming and outgoing arrows. However, there are no states with no outgoing arrows present, so that the UPPAAL model will never be in a deadlock. As a result, the assembly program won’t be stuck in a state and won’t stop until the machine is shut down.

From the UPPAAL model, it is also clear that safety property 4 is correct. The outputs of the H-bridge should never be powered on at the same time, otherwise it will create a short circuit and can’t keep on running. In the UPPAAL model, the H-bridge never shows multiple green lights and continues to run. Therefore, the outputs connected to the H-bridge will never be powered on at the same time, and so there will never be a short circuit.